## Slide 1
Country update
Sweden
Tomas Ekbom, SVEBIO
Stockholm, 31 May 2023

## Slide 2: Stability and sudden changes in policies, mixed signals for investors and actors
Fuel | Comment | Taxes and policy
Petrol | E10, 10% ethanol | Reduction quota mandate 7.8% until 1 Jan 2024
Diesel | B7, 7% FAME + 30-35% HVO | Reduction quota mandate 30.5% until 1 Jan 2024
E85 | Summer: 85% ethanol Winter: 75% ethanol | Full tax exemption for biofuel share to 31 Dec 2026
B100 | RME100 | Full tax exemption to 31 Dec 2026
HVO100 | For some cars and most buses and trucks | Full tax exemption to 31 Dec 2026
ED95 | 95% ethanol for buses and trucks | Full tax exemption to 31 Dec 2026
Bio-CNG | >90% of all bio-CNG is biogas, other is CNG | Full tax exemption to 31 Dec 2030
Road transport shall reduce emissions by 70% until 2030 and Sweden shall get zero net emissions until 2045. Sweden has a climate law and develops a circular bioeconomy. Electrification is underway in transport and industry.

## Slide 3: Biofuels use will drastically drop 2024. Electrification, but hope for e-fuels + SAF.
Bioenergy is Sweden’s largest energy source with 143 TWh, about 39% of consumption. Wind: rapid increase, to 23 TWh 2022. Nuclear: coming back?
Reduction mandate on petrol and diesel is main tool for lowering emissions. In 2022, Sweden got the world’s highest diesel price. Biofuels took most of the blame, the gov then declared 8 May to slash the quotas.
Essentially, the HVO blend will be cut from ca 33 to 2 vol%. All but gone… The result is +5 million ton CO2 emissions, equal to +10% of all emissions...
Four year tax exemption (until 2027) on liquid biofuels for neat biofuels, not blended in petrol and diesel. However, EC has given approval in GEBR?
Electric-charged vehicles have been on the rise, above 50% of new sales. After the bonus were removed the sales are lower, but not much. Total sales plummets.
Still, many new plants and projects, for e-fuels and SAF: 200 000 ton HVO in Gothenburg 2023 and in 2024, 50 000 ton e-methanol in Övik, 1 million ton HVO in Gothenburg, 100 000 ton SAF in Långsele, and 200 000 ton e-methanol at Stenungsund 2025 and 50 000 ton e-SAF 2026. And more.
Year | 2021 | 2022 | 2023 | 2024 | 2023 | 2024 | 2026 | 2027 | 2028 | 2029 | 2030
Petrol | 6% | 7.8% | 10.1% | 12.5% | 7.8% | 6.0% | 19% | 22% | 24% | 26% | 28%
Diesel | 26% | 30.5% | 35% | 40% | 30.5% | 6.0% | 50% | 54% | 58% | 62% | 66%
Red = previous levels